## Slide 1: Master thesis
Dynamic positioning, system identification and control of marine vessels - based on a vessel model

## Slide 2: Presentation
Thesis: Dynamic positioning, system identification and control of marine vessels - based on a vessel model
Candidate: Tommy Sneltvedt
Supervisor: Associate Professor Dr. David Luigi Di Ruscio
Date: 17.11.2025
Time: 09:00-11:00

## Slide 3: Agenda
Brief introduction to DP
Controller algorithms
System identification
Path following and trajectory tracking
Environmentally friendly DP mode
Thruster allocation

## Slide 4: Brief introduction to dynamic positioning
Highlight some key concepts associated with DP

## Slide 5: Dynamic positioning
Dynamic positioning is the art of position keeping.
It is responsible for controlling the thruster inputs to maintain position and attitude in the presence of environmental disturbances.
This is one of the key technologies that makes the modern offshore industry possible.

## Slide 6: Thrusters
Type of thrusters:
Main propellers
Tunnel thrusters
Azimuth thrusters
These thruster can be subdivided into:
Fixed pitch thrusters
Controllable pitch thrusters

## Slide 7: Environmental disturbances
Environmental disturbances:
Wind – Use wind model suggested by Fossen1
Waves – Use random walk model
Current – Use random walk model
1: From the book: “Marine Craft Hydrodynamics and Motion Control”

## Slide 8: Coordinate systems
We consider vessels with three degrees of freedom: surge, sway and yaw.

## Slide 9: Metrics
Integrated Absolute Error (IAE):
Integrated Absolute thruster Force (IAF):
Total Value (TV):
Here X, Y and N refers to net force in surge direction, sway direction and moment in yaw.

## Slide 10: Controller algorithms
Controller algorithms for dynamic positioning

## Slide 11: Twofold control process
Step 1: Calculate the net force in surge and sway, together with the corresponding yaw moment needed for position-keeping.
Step 2: Realize these forces by distributing forces to individual thrusters (thruster allocation).

## Slide 12: Supply model
Supply model
Miscellaneous
SNAME naming convention:
Rotation matrix
This vessel model is related to hydrodynamic added mass (M) and damping (D) as follows:

## Slide 13: DP model (used in Kalman filter)
Same model structure as supply model. The extra row contains the DP current, representing integral action. This is estimated by the Kalman filter. This is an extension of the supply model that includes DP current.
Here, b represent DP current.
Estimated by Kalman filter.

## Slide 14: Control algorithms
LQ optimal control on deviation form.
MPC – Three formulation for estimating the prediction horizon:
  Constant heading for the entire horizon.
  Constant heading rate for the entire horizon.
  Estimate future horizon by calculating future values states previous optimal input u*(tk-1).
  These formulations all use the estimated DP current together with sensor inputs on waves and wind.
NMPC. This method uses the DP current together with sensor inputs on waves and wind.

## Slide 15: LQ optimal control structure

## Slide 16: Control of supply vessel using LQ optimal control (1)
[10, 5, 26°]
[-5, -5, 225°]
t =600
[0, 0, 0°]
t = 100

## Slide 17: Control of supply vessel using LQ optimal control (2)
Setpoint tracking – Shows the north and east position together with the yaw angle
Inputs – Shows input values from controller: force in surge, force in sway, and momentum in yaw.

## Slide 18: MPC/NMPC control structure

## Slide 19: Control of supply vessel using different MPC formulations (1)
[10, 5, 26°]
[-5, -5, 225°]
t =600
[0, 0, 0°]
t = 100

## Slide 20: Control of supply vessel using different MPC formulations (2)
Setpoint tracking – Shows the north and east position together with the yaw angle
Inputs – Shows input values from controller: force in surge, force in sway, and momentum in yaw.

## Slide 21: Control of supply vessel using different NMPC formulations (1)
[-5, 10, -26°]
[5, -5, 135°]
t =600
[0, 0, 0°]
t = 100

## Slide 22: Control of supply vessel using different NPC formulations (2)
Setpoint tracking – Shows the north and east position together with the yaw angle
Inputs – Shows input values from controller: force in surge, force in sway, and momentum in yaw.

## Slide 23: Monte Carlo simulations
To verify that the controller algorithms can handle varying weather conditions and operational demands, Monte Carlo simulations are run a 100 times for each controller.
The setpoint is changes at to time instances t = 100 and t = 600. All these simulations lasts for a 1000 seconds.
The setpoint is moved in some random direction for ten meters both times. The heading setpoint is set equal to this new direction.
Environmental conditions are varied each time since they depend on different seeds for every simulation.

## Slide 24: Summary
Monte Carlo simulation results depicted on the right. LPV and constant rotation formulation are the preferred MPC methods.
NMPC is the most aggressive method here. It shows that there is a tradeoff between lowering setpoint error and total value. This is true for all the algorithms if retuned.

## Slide 25: Summary (2)
It is the author’s experience that the LQ optimal control was the easiest to tune.
It is also the fastest algorithm to run.
Non-linear MPC is both computationally heavy and not trivial to tune. It is the authors opinion the worst solution here. Should only be used for specialized operations like Green DP.

## Slide 26: Demonstration – LQ optimal control

## Slide 27: System identification
Model identification and control based on data collection

## Slide 28: System identification
Step 1: Identify body dynamics
Run open loop simulation with input generated from PRBS1. Identify the relation between the linear and angular velocities:
where,
Step 2: Make new identified vessel model by inserting the identified matrices into the following structure
This can be used in the Kalman filter and model-based controllers (without b term in the LQ optimal controller) to control the original vessel identified.
1: Pseudo Random Binary Signal

## Slide 29: Path plot when identifying model with different identification methods
Three different models identified:
  Supply
  Balchen (nonlinear)
  OSV (nonlinear)
Three different identification methods:
  DSR
  DSR_e
  PEM

## Slide 30: Control of SI identified vessel (supply) using LQ optimal control
Setpoint tracking – Shows the north and east position together with the yaw angle
Inputs – Shows input values from controller: force in surge, force in sway, and momentum in yaw.

## Slide 31: Control of SI identified vessel (OSV) using LQ optimal control
Setpoint tracking – Shows the north and east position together with the yaw angle
Inputs – Shows force in surge, force in sway, and momentum in yaw

## Slide 32: Control of SI identified vessel (Balchen) using LQ optimal control
Setpoint tracking – Shows the north and east position together with the yaw angle
Inputs – Shows input values from controller: force in surge, force in sway, and momentum in yaw.

## Slide 33: Summary
The supply and Balchen model uses net force in surge, net force in sway, and moment in yaw as input.
OSV however uses RPS. Since one unit for input here is equal to many Newtons or Newton-meters, it follows that the tuning becomes very aggressive.
Clearly all identification methods work well (DSR, DSR_e, and PEM).

## Slide 34: Path following and trajectory tracking
Simple algorithms for path following and trajectory tracking

## Slide 35: Algorithms
Path following – The active waypoint is the setpoint.
Trajectory tracking – Waypoints are used to determine setpoints using cubic spline interpolation

## Slide 36: Path following
Path plot – Shows position of the vessel together with waypoints
Setpoint tracking – Shows the north and east position together with the yaw angle

## Slide 37: Trajectory tracking
Path plot – Shows position of the vessel together with waypoints
Setpoint tracking – Shows the north and east position together with the yaw angle

## Slide 38: Summary
LQ optimal control and LPV performs very similar for the path following algorithm (simple).
LPV clearly outperforms LQ optimal control on trajectory tracking (advanced).
No big differences in total value.

## Slide 39: Environmentally friendly DP mode
Also known as green DP in industry

## Slide 40: Green DP
Define the following cost function:
It defines a circular operational area where vessel is allowed to drift with small or no penalty. Movement outside the circle is harshly penalized.

## Slide 41: Comparing two types of weather conditions
Simulation set 1
Simulation set 2
Waves and current are generated by a modified random walk algorithm
With α (reduction factor) set to 0.9.
Waves and current are generated without a reduction factor, i.e., α = 1.
This allows the waves and current forces to drift far away from zero.

## Slide 42: Simulation results from Monte Carlo simulation
Simulation set 1 – Mild weather conditions
Simulation set 2 – Harsher weather conditions

## Slide 43: Thruster allocation
A brief introduction to thruster allocation in the context of LQ optimal control

## Slide 44: Thruster allocation algorithms
Explicit solution
QP solution
Nonlinear programming

## Slide 45: Thruster forces and moment
xb
yb
(1)
(2)
(3)
l1
l2
l3
f3
f1
f2
ͳ3 = l3f3 > 0
ͳ1 = -l1f1 > 0
ͳ2 = -l2f2 < 0

## Slide 46: Thruster configurations
Truster configuration
Truster configuration matrix
Nonrotatable
thrusters
Rotatable
thrusters

## Slide 47: Simulations run here
Setup | Algorithm | Thruster configuration | Comment
L1 | Explicit | Ship configuration 1: Two main propellers and one bow tunnel thruster | 
L2 | Explicit | Ship configuration 2: Two main propellers and two tunnel thruster | 
QP1 | QP | Ship configuration 1: Two main propellers and one bow tunnel thruster | This simulation is not shown here. Same results as L1
QP2 | QP | Ship configuration 2: Two main propellers and two tunnel thruster | Main starboard propeller is limited in output (105 Newton)
Azi | Nonlinear | Ship configuration 3: Two main propellers and two azimuths | 

## Slide 48: Thruster allocation (explicit solution, L1)
[10, 5, 30°]
[0, -5, 45°]
t =600
[0, 0, 0°]
t = 100

## Slide 49: Thruster allocation (explicit solution, L2)
[10, 5, 30°]
[0, -5, 45°]
t =600
[0, 0, 0°]
t = 100

## Slide 50: Thruster allocation (QP solution, Q2)
[10, 5, 30°]
[0, -5, 45°]
t =600
[0, 0, 0°]
t = 100

## Slide 51: Thruster allocation (Nonlinear solution, Azimuth)
[10, 5, 30°]
[0, -5, 45°]
t =600
[0, 0, 0°]
t = 100

## Slide 52: Monte Carlo simulation

## Slide 53: Demonstration – thruster allocation

## Slide 54: Summary
It was shown to be feasible to control vessel using LQ optimal control, MPC and NMPC.
Control of vessel using system identification and model-based controller was shown to be possible. Even for a nonlinear vessel model.
Path following and trajectory tracking is possible. Trajectory tracking works especially well with methods using a prediction horizon.
Green DP can be beneficial under mild weather conditions.
Thruster configuration is important when performing DP. Investing in a proper thruster setup can save significant amounts of fuel.

## Slide 55: Thanks for listening
Any questions?